## Slide 1: CS 61C: Great Ideas in Computer Architecture Intro to Assembly Language, MIPS Intro
Instructors:
Krste Asanovic & Vladimir Stojanovic
http://inst.eecs.Berkeley.edu/~cs61c/sp15

## Slide 2: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions
Logic Circuit Description (Circuit Schematic Diagrams)

## Slide 3: From last lecture …
Computer words and vocabulary are called instructions and instruction set respectively
MIPS is example RISC instruction set used in CS61C
Rigid format: 1 operation, 2 source operands, 1 destination
  add,sub,mul,div,and,or,sll,srl,sra
  lw,sw,lb,sb to move data to/from registers from/to memory
  beq, bne, j, slt, slti for decision/flow control
Simple mappings from arithmetic expressions, array access, in C to MIPS instructions

## Slide 4: Review: Components of a Computer
Processor
Control
Datapath
Program Counter
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
ReadData
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data

## Slide 5: How Program is Stored
Memory
Bytes
Program
Data
One MIPS Instruction = 32 bits

## Slide 6: How Program is Executed: Instruction Fetch
Processor
Control
Datapath
Program Counter
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Bytes
Instruction
Address
Read Instruction Bits
Program
Data
The program counter (internal register inside processor) holds address of next instruction to be executed

## Slide 7: Computer Decision Making
Based on computation, do something different
In programming languages: if-statement
MIPS: if-statement instruction is
beq register1,register2,L1
means: go to statement labeled L1 if (value in register1) == (value in register2)
….otherwise, go to next statement
beq stands for branch if equal
Other instruction: bne for branch if not equal

## Slide 8: Types of Branches
Branch – change of control flow
Conditional Branch – change control flow depending on outcome of comparison
  branch if equal (beq) or branch if not equal (bne)
Unconditional Branch – always branch
  a MIPS instruction for this: jump (j)

## Slide 9: Example if Statement
Assuming translations below, compile if block
f → $s0 g → $s1 h → $s2
i → $s3 j → $s4
if (i == j) bne $s3,$s4,Exit
f = g + h; add $s0,$s1,$s2
Exit:
May need to negate branch condition

## Slide 10: Example if-else Statement
Assuming translations below, compile
f → $s0 g → $s1 h → $s2
i → $s3 j → $s4
if (i == j) bne $s3,$s4,Else
f = g + h; add $s0,$s1,$s2
else j Exit
f = g – h; Else: sub $s0,$s1,$s2
Exit:

## Slide 11: Inequalities in MIPS
Until now, we’ve only tested equalities (== and != in C). General programs need to test < and > as well.
Introduce MIPS Inequality Instruction:
  “Set on Less Than”
  Syntax: slt reg1,reg2,reg3
  Meaning: if (reg2 < reg3) reg1 = 1; else reg1 = 0;
  “set” means “change to 1”, “reset” means “change to 0”.

## Slide 12: Inequalities in MIPS Cont.
How do we use this? Compile by hand: if (g < h) goto Less; #g:$s0, h:$s1
Answer: compiled MIPS code…
slt $t0,$s0,$s1 # $t0 = 1 if g<h bne $t0,$zero,Less # if $t0!=0 goto Less
Register $zero always contains the value 0, so bne and beq often use it for comparison after an slt instruction
sltu treats registers as unsigned

## Slide 13: Immediates in Inequalities
slti an immediate version of slt to test against constants
  Loop: . . . slti $t0,$s0,1 # $t0 = 1 if # $s0<1 beq $t0,$zero,Loop # goto Loop # if $t0==0 # (if ($s0>=1))

## Slide 14: Clickers/Peer Instruction
What is the code above?
A: while loop
B: do … while loop
C: for loop
D: Not a loop
E: Dunno
Label: sll $t1,$s3,2 addu $t1,$t1,$s5 lw $t1,0($t1)
add $s1,$s1,$t1 addu $s3,$s3,$s4 bne $s3,$s2,Label

## Slide 15: Clickers/Peer Instruction
Simple loop in C; A[] is an array of ints
  do { g = g + A[i]; i = i + j; } while (i != h);
Use this mapping: g, h, i, j, &A[0] $s1, $s2, $s3, $s4, $s5
Loop: sll $t1,$s3,2 # $t1= 4*i addu $t1,$t1,$s5 # $t1=addr A+4i lw $t1,0($t1) # $t1=A[i] add $s1,$s1,$t1 # g=g+A[i] addu $s3,$s3,$s4 # i=i+j bne $s3,$s2,Loop # goto Loop # if i!=h

## Slide 16: Six Fundamental Steps in Calling a Function
Put parameters in a place where function can access them
Transfer control to function
Acquire (local) storage resources needed for function
Perform desired task of the function
Put result value in a place where calling program can access it and restore any registers you used
Return control to point of origin, since a function can be called from several points in a program

## Slide 17: MIPS Function Call Conventions
Registers faster than memory, so use them
$a0–$a3: four argument registers to pass parameters
$v0–$v1: two value registers to return values
$ra: one return address register to return to the point of origin
Notes: $at – assembler temporary register, used for pseudo instructions

## Slide 18: Instruction Support for Functions (1/4)
... sum(a,b);... /* a,b:$s0,$s1 */ } int sum(int x, int y) { return x+y; }
address (shown in decimal) 1000 1004 1008 1012 1016 … 2000 2004
C
M I P S
In MIPS, all instructions are 4 bytes, and stored in memory just like data. So here we show the addresses of where the programs are stored.

## Slide 19: Instruction Support for Functions (2/4)
... sum(a,b);... /* a,b:$s0,$s1 */ } int sum(int x, int y) { return x+y; }
address (shown in decimal) 1000 add $a0,$s0,$zero # x = a 1004 add $a1,$s1,$zero # y = b 1008 addi $ra,$zero,1016 #$ra=1016 1012 j sum #jump to sum 1016 … # next instruction … 2000 sum: add $v0,$a0,$a1 2004 jr $ra # new instruction
C
M I P S

## Slide 20: Instruction Support for Functions (3/4)
... sum(a,b);... /* a,b:$s0,$s1 */ } int sum(int x, int y) { return x+y; }
2000 sum: add $v0,$a0,$a1 2004 jr $ra # new instruction
Question: Why use jr here? Why not use j?
Answer: sum might be called by many places, so we can’t return to a fixed place. The calling proc to sum must be able to say “return here” somehow.
C
M I P S

## Slide 21: Instruction Support for Functions (4/4)
Single instruction to jump and save return address: jump and link (jal)
Before: 1008 addi $ra,$zero,1016 #$ra=1016 1012 j sum #goto sum
After: 1008 jal sum # $ra=1012,goto sum
Why have a jal?
  Make the common case fast: function calls very common.
  Don’t have to know where code is in memory with jal!

## Slide 22: MIPS Function Call Instructions
Invoke function: jump and link instruction (jal)
(really should be laj “link and jump”)
  “link” means form an address or link that points to calling site to allow function to return to proper address
  Jumps to address and simultaneously saves the address of the following instruction in register $ra
  jal FunctionLabel
Return from function: jump register instruction (jr)
  Unconditional jump to address specified in register
  jr $ra

## Slide 23: Notes on Functions
Calling program (caller) puts parameters into registers $a0-$a3 and uses jal X to invoke (callee) at address X
Must have register in computer with address of currently executing instruction
  Instead of Instruction Address Register (better name), historically called Program Counter (PC)
  It’s a program’s counter; it doesn’t count programs!
What value does jal X place into $ra? ????
jr $ra puts address inside $ra back into PC
Notes: PC+4

## Slide 24: Where Are Old Register Values Saved to Restore Them After Function Call?
Need a place to save old values before call function, restore them when return, and delete
Ideal is stack: last-in-first-out queue (e.g., stack of plates)
  Push: placing data onto stack
  Pop: removing data from stack
Stack in memory, so need register to point to it
$sp is the stack pointer in MIPS
Convention is grow from high to low addresses
  Push decrements $sp, Pop increments $sp

## Slide 25: Example
int leaf_example (int g, int h, int i, int j)
{
int f;
f = (g + h) – (i + j);
return f;
}
Parameter variables g, h, i, and j in argument registers $a0, $a1, $a2, and $a3, and f in $s0
Assume need one temporary register $t0

## Slide 26: Stack Before, During, After Function
Need to save old values of $s0 and $t0
Contents of $s0
Contents of $t0

## Slide 27: MIPS Code for leaf_example
addi $sp,$sp,-8 # adjust stack for 2 items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
add $t0,$a2,$a3 # t0 = i + j
sub $v0,$s0,$t0 # return value (g + h) – (i + j)
lw $s0, 0($sp) # restore register $s0 for caller
lw $t0, 4($sp) # restore register $t0 for caller
addi $sp,$sp,8 # adjust stack to delete 2 items
jr $ra # jump back to calling routine
Leaf_example
Notes: addi $sp,$sp,-8 # adjust stack for 2 items
sw $t0, 4($sp) # save $t0 for use afterwards
sw $s0, 0($sp) # save $s0 for use afterwards
add $s0,$a0,$a1 # f = g + h
add $t0,$a2,$a3 # t0 = i + j
sub $v0,$s0,$t0 # return value (g + h) – (i + j)
lw $s0, 0($sp) # restore register $s0 for caller
lw $t0, 4($sp) # restore register $t0 for caller
addi $sp,$sp,8 # adjust stack to delete 2 items
jr $ra # jump back to calling routine

## Slide 28: What If a Function Calls a Function? Recursive Function Calls?
Would clobber values in $a0 to $a3 and $ra
What is the solution?
Notes: Save $ra on the stack

## Slide 29: Nested Procedures (1/2)
int sumSquare(int x, int y) { return mult(x,x)+ y; }
Something called sumSquare, now sumSquare is calling mult.
So there’s a value in $ra that sumSquare wants to jump back to, but this will be overwritten by the call to mult.
Need to save sumSquare return address before call to mult.

## Slide 30: Nested Procedures (2/2)
In general, may need to save some other info in addition to $ra.
When a C program is run, there are 3 important memory areas allocated:
  Static: Variables declared once per program, cease to exist only after execution completes - e.g., C globals
  Heap: Variables declared dynamically via malloc
  Stack: Space to be used by procedure during execution; this is where we can save register values

## Slide 31: Optimized Function Convention
To reduce expensive loads and stores from spilling and restoring registers, MIPS divides registers into two categories:
Preserved across function call
  Caller can rely on values being unchanged
  $ra, $sp, $gp, $fp, “saved registers” $s0- $s7
Not preserved across function call
  Caller cannot rely on values being unchanged
  Return value registers $v0,$v1, Argument registers $a0-$a3, “temporary registers” $t0-$t9

## Slide 32: Clickers/Peer Instruction
Which statement is FALSE?
B: jal saves PC+1 in $ra
C: The callee can use temporary registers ($ti) without saving and restoring them
A: MIPS uses jal to invoke a function and jr to return from a function
D: The caller can rely on the saved registers ($si) without fear of callee changing them
Notes: B: Print It saves PC+4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only increment 1.

## Slide 33: Clickers/Peer Instruction
Which statement is FALSE?
B: jal saves PC+1 in $ra
C: The callee can use temporary registers ($ti) without saving and restoring them
A: MIPS uses jal to invoke a function and jr to return from a function
D: The caller can rely on the saved registers ($si) without fear of callee changing them
Notes: B: Print It saves PC+4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only increment 1.

## Slide 34: Administrivia
Hopefully everyone turned-in HW0
HW1 due 11:59:59pm Sunday 2/8

## Slide 35: In the News MIPS for hobbyists
MIPS Creator CI20 dev board now available
  A lot like Raspberry Pi but with MIPS CPU
  Supports Linux and Android
1.2GHz 32-bit MIPS with integrated graphics
http://liliputing.com/2015/01/mips-creator-ci20-dev-board-now-available-for-65.html

## Slide 36: Allocating Space on Stack
C has two storage classes: automatic and static
  Automatic variables are local to function and discarded when function exits
  Static variables exist across exits from and entries to procedures
Use stack for automatic (local) variables that don’t fit in registers
Procedure frame or activation record: segment of stack with saved registers and local variables
Some MIPS compilers use a frame pointer ($fp) to point to first word of frame

## Slide 37: Stack Before, During, After Call

## Slide 38: Using the Stack (1/2)
So we have a register $sp which always points to the last used space in the stack.
To use stack, we decrement this pointer by the amount of space we need and then fill it with info.
So, how do we compile this?
  int sumSquare(int x, int y) { return mult(x,x)+ y; }

## Slide 39: Using the Stack (2/2)
Hand-compile sumSquare: addi $sp,$sp,-8 # space on stack sw $ra, 4($sp) # save ret addr sw $a1, 0($sp) # save y add $a1,$a0,$zero # mult(x,x) jal mult # call mult lw $a1, 0($sp) # restore y add $v0,$v0,$a1 # mult()+y lw $ra, 4($sp) # get ret addr addi $sp,$sp,8 # restore stack jr $ra mult: ...
  int sumSquare(int x, int y) { return mult(x,x)+ y; }
“push”
“pop”

## Slide 40: Basic Structure of a Function
entry_label: addi $sp,$sp, -framesize sw $ra, framesize-4($sp) # save $ra save other regs if need be
...
restore other regs if need be lw $ra, framesize-4($sp) # restore $ra addi $sp,$sp, framesize jr $ra
Epilogue
Prologue
Body (call other functions…)
ra
memory

## Slide 41: Where is the Stack in Memory?
MIPS convention
Stack starts in high memory and grows down
  Hexadecimal (base 16) : 7fff fffchex
MIPS programs (text segment) in low end
  0040 0000hex
static data segment (constants and other static variables) above text for static variables
  MIPS convention global pointer ($gp) points to static
Heap above static for data structures that grow and shrink ; grows up to high addresses

## Slide 42: MIPS Memory Allocation

## Slide 43: Register Allocation and Numbering

## Slide 44: And in Conclusion…
Functions called with jal, return with jr $ra.
The stack is your friend: Use it to save anything you need. Just leave it the way you found it!
Instructions we know so far…
  Arithmetic: add, addi, sub, addu, addiu, subu
  Memory: lw, sw, lb, sb
  Decision: beq, bne, slt, slti, sltu, sltiu
  Unconditional Branches (Jumps): j, jal, jr
Registers we know so far
  All of them!
  $a0-$a3 for function arguments, $v0-$v1 for return values
  $sp, stack pointer, $fp frame pointer, $ra return address

## Slide 45: Bonus Slides

## Slide 46: Recursive Function Factorial
int fact (int n)
{
if (n < 1) return (1);
else return (n * fact(n-1));
}

## Slide 47: Recursive Function Factorial
Fact: # adjust stack for 2 items
addi $sp,$sp,-8
# save return address
sw $ra, 4($sp) # save argument n
sw $a0, 0($sp) # test for n < 1
slti $t0,$a0,1
# if n >= 1, go to L1
beq $t0,$zero,L1 # Then part (n==1) return 1
addi $v0,$zero,1 # pop 2 items off stack
addi $sp,$sp,8 # return to caller
jr $ra
L1:
# Else part (n >= 1) # arg. gets (n – 1)
addi $a0,$a0,-1 # call fact with (n – 1)
jal fact
# return from jal: restore n
lw $a0, 0($sp) # restore return address
lw $ra, 4($sp) # adjust sp to pop 2 items
addi $sp, $sp,8 # return n * fact (n – 1)
mul $v0,$a0,$v0 # return to the caller
jr $ra
mul is a pseudo instruction
Notes: Slti: set dst to 1 if src is less than imm (signed immediate)