## Slide 1: CS 61C: Great Ideas in Computer Architecture (Machine Structures) Caches Part 2
Instructors:
Krste Asanovic & Vladimir Stojanovic
http://inst.eecs.berkeley.edu/~cs61c/

## Slide 2: You Are Here!
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Main Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s
Lecture

## Slide 3: Caches Review
Principle of Locality
  Temporal Locality and Spatial Locality
Hierarchy of Memories (speed/size/cost per bit) to Exploit Locality
Cache – copy of data in lower level of memory hierarchy
Direct Mapped to find block in cache using Tag field and Valid bit for Hit
Cache design choice:
  Write-Through vs. Write-Back

## Slide 4: Review: Adding Cache to Computer
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
ReadData
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data
Cache

## Slide 5: Processor Address Fields used by Cache Controller
Block Offset: Byte address within block
Set Index: Selects which set
Tag: Remaining portion of processor address
Size of Index = log2 (number of sets)
Size of Tag = Address size – Size of Index – log2 (number of bytes/block)
Block offset
Set Index
Tag
Processor Address (32-bits total)
Notes: For class handout

## Slide 6: Review: Direct-Mapped Cache
One word blocks, cache size = 1K words (or 4KB)
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Block offset
20
Data
32
Hit
Valid bit ensures something useful in cache for this index
Compare Tag with upper part of Address to see if a Hit
Read data from cache instead of memory if a Hit
Comparator
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 K word (4Kbyte) direct mapped cache with block size equals to 4 bytes (1 word).
In other words, each block associated with the cache tag will have 4 bytes in it (Row 1).
With Block Size equals to 4 bytes, the 2 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K word, the upper 32 minus 10+2 bits, or 20 bits of the address will be stored as cache tag.
The rest of the (10) address bits in the middle, that is bit 2 through 11, will be used as Cache Index to select the proper cache entry
Temporal!

## Slide 7: Cache Terms
Hit rate: fraction of accesses that hit in the cache
Miss rate: 1 – Hit rate
Miss penalty: time to replace a block from lower level in memory hierarchy to cache
Hit time: time to access cache memory (including tag comparison)
Abbreviation: “$” = cache (A Berkeley innovation!)

## Slide 8: Average Memory Access Time (AMAT)
Average Memory Access Time (AMAT) is the average to access memory considering both hits and misses in the cache
  AMAT = Time for a hit + Miss rate x Miss penalty
Notes: AMAT = 1 + 0.02x50 = 2

## Slide 9
B: 400 psec
C: 600 psec
D: ≥ 800 psec
A: ≤200 psec
☐
☐
☐
☐
Clickers/Peer instruction
  AMAT = Time for a hit + Miss rate x Miss penalty
Given a 200 psec clock, a miss penalty of 50 clock cycles, a miss rate of 0.02 misses per instruction and a cache hit time of 1 clock cycle, what is AMAT?
Notes: VertLeftWhiteCheck1
B: Print It saves PC+4 …because ints in this system are 4-bytes long and the actual address increments by 4 even though it appears to only incrememt 1.

## Slide 10: Example: Direct-Mapped $ with 4 Single-Word Lines, Worst-Case Reference String
0
4
0
4
0
4
0
4
Consider the main memory address reference string
  0 4 0 4 0 4 0 4
Start with an empty cache - all blocks initially marked as not valid
Notes: For class handout

## Slide 11: Example: Direct-Mapped $ with 4 Single-Word Lines, Worst-Case Reference String
0
4
0
4
0
4
0
4
Consider the main memory address reference string
  0 4 0 4 0 4 0 4
miss
miss
miss
miss
miss
miss
miss
miss
00 Mem(0)
00 Mem(0)
01
4
01 Mem(4)
0
00
00 Mem(0)
01
4
00 Mem(0)
01
4
00 Mem(0)
01
4
01 Mem(4)
0
00
01 Mem(4)
0
00
Start with an empty cache - all blocks initially marked as not valid
Ping-pong effect due to conflict misses - two memory locations that map into the same cache block
  8 requests, 8 misses
Notes: For class handout

## Slide 12: Alternative Block Placement Schemes
DM placement: mem block 12 in 8 block cache: only one cache block where mem block 12 can be found—(12 modulo 8) = 4
SA placement: four sets x 2-ways (8 cache blocks), memory block 12 in set (12 mod 4) = 0; either element of the set
FA placement: mem block 12 can appear in any cache blocks

## Slide 13: Example: 2-Way Set Associative $ (4 words = 2 sets x 2 ways per set)
0
Cache
Main Memory
Q: How do we find it?
Use next 1 low order memory address bit to determine which cache set (i.e., modulo the number of sets in the cache)
Tag
Data
Q: Is it there?
Compare all the cache tags in the set to the high order 3 memory address bits to tell if the memory block is in the cache
V
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Set
1
0
1
Way
0
1
One word blocks
Two low order bits define the byte in the word (32b words)
Notes: For lecture
This picture is as opposed to
Way 0
both red Set 0
Way 1
------------------------------------
Way 0
both green Set 1
Way 1

## Slide 14: Example: 4 Word 2-Way SA $ Same Reference String
0
4
0
4
Consider the main memory word reference string
  0 4 0 4 0 4 0 4
Start with an empty cache - all blocks initially marked as not valid
Notes: For class handout

## Slide 15: Example: 4-Word 2-Way SA $ Same Reference String
0
4
0
4
Consider the main memory address reference string
  0 4 0 4 0 4 0 4
miss
miss
hit
hit
000 Mem(0)
000 Mem(0)
Start with an empty cache - all blocks initially marked as not valid
010 Mem(4)
010 Mem(4)
000 Mem(0)
000 Mem(0)
010 Mem(4)
Solves the ping-pong effect in a direct-mapped cache due to conflict misses since now two memory locations that map into the same cache set can co-exist!
  8 requests, 2 misses
Notes: For lecture
Another sample string to try 0 1 2 3 0 8 11 0 3

## Slide 16: Different Organizations of an Eight-Block Cache
Total size of $ in blocks is equal to number of sets x associativity. For fixed $ size, increasing associativity decreases number of sets while increasing number of elements per set. With eight blocks, an 8-way set-associative $ is same as a fully associative $.

## Slide 17: Four-Way Set-Associative Cache
28 = 256 sets each with four ways (each with one block)
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Index
Data
Tag
V
0
1
2
.
.
.
253
254
255
8
Index
22
Tag
Hit
Data
32
4x1 select
Way 0
Way 1
Way 2
Way 3
Notes: This is called a 4-way set associative cache because there are four cache entries for each cache index. Essentially, you have four direct mapped cache working in parallel.
This is how it works: the cache index selects a set from the cache. The four tags in the set are compared in parallel with the upper bits of the memory address.
If no tags match the incoming address tag, we have a cache miss.
Otherwise, we have a cache hit and we will select the data from the way where the tag matches occur.
This is simple enough. What is its disadvantages?
+1 = 36 min. (Y:16)

## Slide 18: Range of Set-Associative Caches
For a fixed-size cache, each increase by a factor of two in associativity doubles the number of blocks per set (i.e., the number or ways) and halves the number of sets – decreases the size of the index by 1 bit and increases the size of the tag by 1 bit
Word offset
Byte offset
Index
Tag
Notes: For class handout

## Slide 19: Range of Set-Associative Caches
For a fixed-size cache, each increase by a factor of two in associativity doubles the number of blocks per set (i.e., the number or ways) and halves the number of sets – decreases the size of the index by 1 bit and increases the size of the tag by 1 bit
Word offset
Byte offset
Index
Tag
Decreasing associativity
Fully associative
(only one set)
Tag is all the bits except
block and byte offset
Direct mapped
(only one way)
Smaller tags, only a single comparator
Increasing associativity
Selects the set
Used for tag compare
Selects the word in the block
Notes: For lecture
In 2008, the greater size and power consumption of CAMs generally leads to 2-way and 4-way set associativity being built from standard SRAMs with comparators with 8-way and above being built using CAMs

## Slide 20: Costs of Set-Associative Caches
N-way set-associative cache costs
  N comparators (delay and area)
  MUX delay (set selection) before data is available
  Data available after set selection (and Hit/Miss decision). DM $: block is available before the Hit/Miss decision
    In Set-Associative, not possible to just assume a hit and continue and recover later if it was a miss
When miss occurs, which way’s block selected for replacement?
  Least Recently Used (LRU): one that has been unused the longest (principle of temporal locality)
    Must track when each way’s block was used relative to other blocks in the set
    For 2-way SA $, one bit per set → set to 1 when a block is referenced; reset the other way’s bit (i.e., “last used”)
Notes: First of all, a N-way set associative cache will need N comparators instead of just one comparator (use the right side of the diagram for direct mapped cache).
A N-way set associative cache will also be slower than a direct mapped cache because of this extra multiplexer delay.
Finally, for a N-way set associative cache, the data will be available AFTER the hit/miss signal becomes valid because the hit/mis is needed to control the data MUX.
For a direct mapped cache, that is everything before the MUX on the right or left side, the cache block will be available BEFORE the hit/miss signal (AND gate output) because the data does not have to go through the comparator.
This can be an important consideration because the processor can now go ahead and use the data without knowing if it is a Hit or Miss. Just assume it is a hit.
Since cache hit rate is in the upper 90% range, you will be ahead of the game 90% of the time and for those 10% of the time that you are wrong, just make sure you can recover.
You cannot play this speculation game with a N-way set-associative cache because as I said earlier, the data will not be available to you until the hit/miss signal is valid.
+2 = 38 min. (Y:18)

## Slide 21: Cache Replacement Policies
Random Replacement
  Hardware randomly selects a cache evict
Least-Recently Used
  Hardware keeps track of access history
  Replace the entry that has not been used for the longest time
  For 2-way set-associative cache, need one bit for LRU replacement
Example of a Simple “Pseudo” LRU Implementation
  Assume 64 Fully Associative entries
  Hardware replacement pointer points to one cache entry
  Whenever access is made to the entry the pointer points to:
    Move the pointer to the next entry
  Otherwise: do not move the pointer
  (example of “not-most-recently used” replacement policy)
:
Entry 0
Entry 1
Entry 63
Replacement
Pointer

## Slide 22: Benefits of Set-Associative Caches
Choice of DM $ or SA $ depends on the cost of a miss versus the cost of implementation
Largest gains are in going from direct mapped to 2-way (20%+ reduction in miss rate)
Notes: As cache sizes grow, the relative improvement from associativity increases only slightly; since the overall miss rate of a larger cache is lower, the opportunity for improving the miss rate decreases and the absolute improvement in miss rate from associativity shrinks significantly.

## Slide 23: Administrivia
Project 2-1 due Sunday March 15th, 11:59PM
  Use pinned Piazza threads!
  We’ll penalize those who ask, but don’t search!
Guerilla sections starting this weekend
  Optional sections, focus on lecture/exam material, not projects
  Vote for time slot on Piazza poll

## Slide 24: Understanding Cache Misses: The 3Cs
Compulsory (cold start or process migration, 1st reference):
  First access to block impossible to avoid; small effect for long running programs
  Solution: increase block size (increases miss penalty; very large blocks could increase miss rate)
Capacity:
  Cache cannot contain all blocks accessed by the program
  Solution: increase cache size (may increase access time)
Conflict (collision):
  Multiple memory locations mapped to the same cache location
  Solution 1: increase cache size
  Solution 2: increase associativity (may increase access time)
Notes: (Capacity miss) That is the cache misses are due to the fact that the cache is simply not large enough to contain all the blocks that are accessed by the program.
The solution to reduce the Capacity miss rate is simple: increase the cache size.
Here is a summary of other types of cache miss we talked about.
First is the Compulsory misses. These are the misses that we cannot avoid. They are caused when we first start the program.
Then we talked about the conflict misses. They are the misses that caused by multiple memory locations being mapped to the same cache location.
There are two solutions to reduce conflict misses. The first one is, once again, increase the cache size. The second one is to increase the associativity.
For example, say using a 2-way set associative cache instead of directed mapped cache.
But keep in mind that cache miss rate is only one part of the equation. You also have to worry about cache access time and miss penalty. Do NOT optimize miss rate alone.
Finally, there is another source of cache miss we will not cover today. Those are referred to as invalidation misses caused by another process, such as IO , update the main memory so you have to flush the cache to avoid inconsistency between memory and cache.
+2 = 43 min. (Y:23)

## Slide 25: How to Calculate 3C’s using Cache Simulator
Compulsory: set cache size to infinity and fully associative, and count number of misses
Capacity: Change cache size from infinity, usually in powers of 2, and count misses for each reduction in size
  16 MB, 8 MB, 4 MB, … 128 KB, 64 KB, 16 KB
Conflict: Change from fully associative to n-way set associative while counting misses
  Fully associative, 16-way, 8-way, 4-way, 2-way, 1-way

## Slide 26: 3Cs Analysis
Three sources of misses (SPEC2000 integer and floating-point benchmarks)
  Compulsory misses 0.006%; not visible
  Capacity misses, function of cache size
  Conflict portion depends on associativity and cache size

## Slide 27: Improving Cache Performance
Reduce the time to hit in the cache
  E.g., Smaller cache
Reduce the miss rate
  E.g., Bigger cache
Reduce the miss penalty
  E.g., Use multiple cache levels
  AMAT = Time for a hit + Miss rate x Miss penalty

## Slide 28: Impact of Larger Cache on AMAT?
1) Reduces misses (what kind(s)?)
2) Longer Access time (Hit time): smaller is faster
  Increase in hit time will likely add another stage to the pipeline
At some point, increase in hit time for a larger cache may overcome the improvement in hit rate, yielding a decrease in performance
Computer architects expend considerable effort optimizing organization of cache hierarchy – big impact on performance and power!
Notes: AMAT = 1 + 0.02x50 = 2

## Slide 29: Clickers: Impact of longer cache blocks on misses?
For fixed total cache capacity and associativity, what is effect of longer blocks on each type of miss:
  A: Decrease, B: Unchanged, C: Increase
Compulsory?
Capacity?
Conflict?

## Slide 30: Clickers: Impact of longer blocks on AMAT
For fixed total cache capacity and associativity, what is effect of longer blocks on each component of AMAT:
  A: Decrease, B: Unchanged, C: Increase
Hit Time?
Miss Rate?
Miss Penalty?

## Slide 31: Clickers/Peer Instruction: For fixed capacity and fixed block size, how does increasing associativity effect AMAT?
A: Increases hit time, decreases miss rate
B: Decreases hit time, decreases miss rate
C: Increases hit time, increases miss rate
D: Decreases hit time, increases miss rate

## Slide 32: Cache Design Space
Several interacting dimensions
  Cache size
  Block size
  Associativity
  Replacement policy
  Write-through vs. write-back
  Write allocation
Optimal choice is a compromise
  Depends on access characteristics
    Workload
    Use (I-cache, D-cache)
  Depends on technology / cost
Simplicity often wins
Associativity
Cache Size
Block Size
Bad
Good
Less
More
Factor A
Factor B
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.

## Slide 33: And, In Conclusion …
Name of the Game: Reduce AMAT
  Reduce Hit Time
  Reduce Miss Rate
  Reduce Miss Penalty
Balance cache parameters (Capacity, associativity, block size)